## Slide 1: Accumulator Walk Through
Anthony Winchester

## Slide 2: The Accumulator
Processor register
Contains one operand (The quantity on which an arithmetic or logical operation is to be done)
Used to store the result of an operation
Generally denoted as AC, but can be any register name

## Slide 3: Example 1

## Slide 4: LOAD D
AC <- D
Value in D is written to the accumulator
Accumulator holds the value of D
D
AC

## Slide 5: MPY E
AC <- AC*E
Value in E is multiplied by the value in the accumulator
Result of multiplication is written back into accumulator
D*E
AC

## Slide 6: ADD C
AC <- AC +C
Value in C is added to the value in the accumulator
Result of addition is written back into accumulator
AC
(D*E)+C

## Slide 7: STOR Y
Y <-AC
The value in the accumulator is moved to Y for storage
The accumulator is empty again
AC
y
(D*E)+C

## Slide 8: LOAD A
AC <- A
Value in A is written to the accumulator
Accumulator holds value of A
Storage spot Y still storing first result
AC
y
(D*E)+C
A

## Slide 9: SUB B
AC <-AC – B
Value in B is subtracted from the value in the accumulator
Result of subtraction is written back into accumulator
AC
y
(D*E)+C
A-B

## Slide 10: DIV Y
AC <- AC/y
Value in accumulator is divided by the value stored in y
Result of division is written back into accumulator
AC
y
(D*E)+C
A-B
(D*E)+C

## Slide 11: STOR Y
Y <- AC
Again, the value in the accumulator is moved into y for storage
The accumulator AC is empty once again
AC
y
(D*E)+C
A-B

## Slide 12: Example 2
Do you remember Program 8a?
Contains an accumulator register R0
R0 is where the logical OR was performed
Result placed back into R0

## Slide 13: The _togglecase: Section
_togglecase:
  LDR R1, = String @address of char
  LDR R0, [R1] @load it into R0
  ORR R0,R0,#0x20 @Change case
  STR R0, [R1] @Write char back

## Slide 14: Take A Closer Look
LDR R1, = string
  Load Register R1 with the address of the label = string
LDR R0,[R1]
  Load Register R0, R0 with the value of Register R1
ORR R0,R0,#0x20
  Do logical OR on value in Register R0 with Hex value w (0X20)
  Put result back into Register R0
STR R0,[R1]
  STORE the value in Register R0 into Register R1