## Slide 1: Lecture – All About Robot Motors
CAC 240
Anthony Winchester

## Slide 2: What Do Motors Do?
Most common actuators in robotics
Causes robots to take action
Used to make wheels and other effectors move
Uses more power (current) to run than electronics do
Small DC motor draws 100 milliamps up to 1 amp of current
Small microprocessors can draw 5 milliamps of current (much less)

## Slide 3: Various Types of Motors

## Slide 4: Direct Current (DC) Motors
Converts electrical energy into mechanical energy
  Using magnets, wire loops, and current
  Generates magnetic fields
  Interaction turns the motor shaft and generates kinetic energy
Simple, inexpensive, easy to find
Power it up with electricity in the right voltage range

## Slide 5: Work = Force * Distance
Physics definition

## Slide 6: More about DC Motors
When a DC motor is provided with constant voltage in the right range, it draws current in the amount proportional to the work it is doing
  Robot pushing against a wall doing more work than a robot moving freely with no obstacles
  Current is higher because of wall resistance
Robots need to do work
  Pull their body load
  Turn their wheels
  Lift their manipulators
  Motors need to turn fast (up to 150 revolutions per second)

## Slide 7: Motor Power
Amount of power used = rotational force (torque) * rotational velocity
  When motor spins freely, rotational velocity is at highest level, but torque is zero = Power used is also zero
  When motor stalls, torque is at max level, but rotational velocity is zero = Power used is also zero

## Slide 8: Servo Motors
Motors that turn shaft to a certain position
Used very effectively in toys
  Effector moves to a certain place and stops or takes some type of action
  Adjusting steering in remote controlled cars
  Adjusting wing position in remote controlled airplanes

## Slide 9: Servo Motors (continued)
Servo motors are made from DC motors with three additions:
  Gear reduction
  Position sensor for the motor shaft
    Tracks how much motor is turning
    Tracks direction of motor
  Electronic circuit to control motor
    Tells motor how much to turn and in what direction

## Slide 10: Turning Radius of Servo Motor
Servo motors are limited to only turning 180 degrees
  Moves the shaft to the desired position
Turning radius determined by electric signal made up of pulses
  When pulses arrive at motor, the motor turns
  When no pulses arrive, the motor stops moving
  This pattern of pulses produces a waveform

## Slide 11: Pulse – Width Modulation
Duration of pulse determines the amount that the motor shaft turns
The width (duration) of the pulse modulates (controls) the signal
  Exact width of pulse is very important
  Uneven width of pulse can cause motor to behave poorly

## Slide 12: Position Control & Torque Control
Position Control: Motor is driven to track desired position at all times
  Makes motor driven actuators very accurate
  Causes actuator to be stiff
Torque Control: Motor is driven to track the desired rotational force at all times (regardless of position)
  Makes actuator much less stiff

## Slide 13: Make sure you go through this information on motors
It might show up on our Midterm exam in March