## Slide 1: Initial Module Testing of Freenove Smart Car
CAC 240
Anthony Winchester

## Slide 2: The car is ready. Let’s hit it with some module tests to make sure it works!

## Slide 3: Hang on. What Is Module testing?
Type of software testing
Checks individual subprograms, subroutines, classes, or procedures in a program
Main objectives:
Ensures module is fully tested
Verifies functionality of module
Preparation for full Application testing

## Slide 4: Benefits of Module Testing
If you test small piece, much easier to identify, understand and fix the defects at the module level
Can pinpoint issues
Multiple modules can be tested in parallel independent of each other
Individual modules assigned to different people to test at same time
Huge time saver

## Slide 5: BEFORE we test…We Gotta Connect!
Make sure the two blue switches (on the right side of the robot car when the ultrasonic sensor is facing you) are pressed down.
1
Connect monitor to the Raspberry Pi using the HDMI cable.
2
Connect mouse to the Raspberry Pi through the USB port.
3
Connect the keyboard to the Raspberry Pi through the USB port.
4
Ensure batteries are installed so that the Raspberry Pi has power.
5

## Slide 6: BEFORE we test…We Gotta Connect (continued)
The Raspberry Pi will start the boot process.
After the boot process completes, you may be asked to login:
  Username: pi
  Password: raspberry
  Press Enter to login

## Slide 7: Connecting via Laptop
Bit more difficult to connect via your personal laptop
Need the IP address of Raspberry Pi
In class: multiple Raspberry Pi boards connected to network
At home: can see wifi connection via router software (example: home router app on cell phone)
Open Remote Desktop Connection on personal laptop
Click on “Type here to search” next to the Start Window and search for the word Remote
Enter IP address of Raspberry Pi found above and click “Connect”
Message: “Identity of remote computer cannot be verified; connect anyway?” – click on OK
Login screen appears
Use previous slide to log in

## Slide 8: Connect to WiFi
After login, connect to WiFi.
  On the upper right corner, click the middle icon
  It may ask you to “Turn On Wireless LAN”, if so, click on that option.
  You may need to select the middle icon again if you had to turn ON the wireless LAN.
  A list of wireless connections will appear. Select the connection for our area.

## Slide 9: First Three Module Tests from Configuration Document
We will execute these tests together in class

## Slide 10: Motor Test
The car must be equipped with batteries, and both blue switches (S1 power switch and S2 motor switch) need to be pressed in the down position. The 5V, 3.3V, battery power indicators will light up.
A few notes:
  On the robots, the direction in the result section below will be REVERSED:
    It moves backward first, then it moves forward.
    Code fix in later slide….
  During the test, the motor will move the car, so please be careful if sitting on desk!
  If you notice that the car is not working, please check both switches to be sure they are in the down position.

## Slide 11: Motor Test (continued)
On the left side of the environment screen, click on the black box on the upper left side to open Raspberry Pi terminal.
Enter the following commands to test the motor:
  cd ~/Freenove_4WD_Smart_Car_Kit_for_Raspberry_Pi/Code/Server <press enter>
  sudo python test.py Motor <press enter>
Result:
  The car moves forward for 1 second, then moves back for 1 second, then turns left for 1 second, turns right for 1 second, then stops.

## Slide 12: Motor Test (code fix)
On upper left side, click on the folder icon.
Navigate to Motor.py in the following path in your Raspberry Pi:
  Freenove_4WD_Smart_Car_Kit_for_Raspberry_Pi/Code/Server/Motor.py
Open Motor.py using the text editor and find the function “setMotorModel”
Add a minus sign (“–“) before duty1, duty2, duty3, and duty 4 (as shown on right side).
Save and run the two commands on the previous slide again.
def setMotorModel(self,duty1,duty2,duty3,duty4):
  duty1,duty2,duty3,duty4=self.duty_range(duty1,duty2,duty3,duty4)
  self.left_Upper_Wheel(-duty1)
  self.left_Lower_Wheel(-duty2)
  self.right_Upper_Wheel(-duty3)
  self.right_Lower_Wheel(-duty4)

## Slide 13: Photoresistor Test
Enter the following commands in the Raspberry Pi terminal to test ADC module for light tracking:
  cd ~/Freenove_4WD_Smart_Car_Kit_for_Raspberry_Pi/Code/Server <press enter>
  sudo python test.py ADC <press enter>
Result:
  Every second, the voltage values of the two photoresistors and the battery are output.
  NOTE: When you are just starting up the Raspberry Pi, these values may be inaccurate at first. It will become stable later. Press "Ctrl + C" to end execution.

## Slide 14: Buzzer Functionality Test
Enter the following set of commands in the Raspberry Pi terminal to test the buzzer:
  cd ~/Freenove_4WD_Smart_Car_Kit_for_Raspberry_Pi/Code/Server <press enter>
  sudo python test.py Buzzer <press enter>
Result:
  The buzzer will turn on and last for 3 seconds, then it will turn back off automatically. You can also press "Ctrl + C" to end program execution.