## Slide 1: Pulse Width Modulation for Robots
CAC 240
Anthony Winchester

## Slide 2: What is Pulse Width Modulation (PWM)?
Method of reducing the average power delivered by an electrical signal, by effectively chopping it up into discrete parts
Average value of voltage (and current) fed to the load is controlled by turning the switch between supply and load on and off at a fast rate
The longer the switch is on compared to the off periods, the higher the total power supplied to the load

## Slide 3: Use in Electronics
Modern microcontrollers (MCUs) integrate PWM controllers exposed to external pins as peripheral devices under firmware control by means of internal programming interfaces
Commonly used for direct current (DC) motor control in robotics
Can control dimming of RGB LEDs
Also used for servo control
  Servo is sent a PWM (pulse-width modulation) signal

## Slide 4: Duty Cycle
Duty cycle describes the proportion of 'on' time to the regular interval or 'period' of time
Described as percentage
This period of time is the inverse of the frequency of the waveform

## Slide 5: What Duty Cycle Looks Like
If digital signal spends half of the time on and the other half off, the digital signal has a duty cycle of 50% and resembles an ideal square wave
If the percentage is higher than 50%, the digital signal spends more time in the high state than the low state
If the percentage is lower than 50%, the digital signal spends more time in the low state than the high state

## Slide 6: Using PWM with Motors
Motor is a varying electrical load.
  Needs a lot more power at startup that it does when running
  Also draws a lot more power when a robot goes uphill or pushes something
Resistors not good choice for controlling power delivered to a large load
  As the power requirements increase, resistor power rating will quickly be exceeded, electronic component will get very hot, and will likely fail permanently.
  Resistor wastes excess power as heat (not ideal for battery powered robot)

## Slide 7: Running Motor using PWM
By using a transistor (Q3), the speed of the motor can be controlled by the duty cycle of the square wave.
A diode, D3, has been added to reroute inductive motor spikes.
In this schematic, the motor can receive up to 12V even though the logic chip is only powered by 5V. This is possible because the logic chip output feeds into the resistor of the transistor, not directly to the motor. The resistor (R3), transistor (Q3), and diode (D3) all help isolate the logic voltages from the motor voltages.