## Slide 1: Junction Field Effect Transistor (JFET)
CAC 240
Anthony Winchester

## Slide 2: What is a Junction Field Effect Transistor?
Voltage controlled three terminal unipolar semiconductor device
Contains a narrow piece of high resistivity semiconductor material
Forms a “channel” of either N-type or P-type silicon
Allows majority carriers to flow through with two ohmic electrical connections at either end
  Drain
  Source
Also, third electrical connection called the Gate terminal

## Slide 3: Two Basic JFET Configurations
P-channel JFET
  Acceptor impurities added to semiconductor
  Flow of current through the channel is positive (hence the term P-channel) in the form of holes
N-channel JFET
  Donor impurities added to semiconductor
  Flow of current through the channel is negative (hence the term N-channel) in the form of electrons
  More efficient conductor compared to their P-channel counterparts
    Greater channel conductivity (lower resistance) than their equivalent P-channel types
    Electrons have a higher mobility through a conductor compared to holes

## Slide 4: Junction Field Effect Transistor
Semiconductor “channel” of the Junction Field Effect Transistor is a resistive path through which a voltage causes a current to flow
The junction field effect transistor can conduct current equally well in either direction
Voltage gradient is formed down the length of the channel,becoming less positive as we go from the Drain terminal to the Source terminal
Result: the PN-junction has a high reverse bias at the Drain terminal and a lower reverse bias at the Source terminal
  Bias causes a “depletion layer” to be formed within the channel
  Depletion layer width increases with the bias

## Slide 5: Current Flow of JFET
Magnitude of the current flowing through the channel between the Drain and the Source terminals is controlled by a voltage applied to the Gate terminal, which is a reverse-biased
  N-channel JFET - Gate voltage is negative
  P-channel JFET - Gate voltage is positive
Because a Junction Field Effect Transistor (JFET) is a voltage-controlled device, NO current flows into the Gate Terminal
  Source current flowing out of the device = Drain current flowing into the device

## Slide 6: JFET Diagrams
N-Channel JFET
P-Channel JFET

## Slide 7: Four Regions for JFET
Ohmic Region
When the voltage between the Gate and the Source is 0, the depletion layer of the channel is very small and the JFET acts like a voltage-controlled resistor
Cut-off Region
Also known as the pinch-off region where the Gate voltage is sufficient for the JFET to act as an open circuit because channel resistance is at max
Saturation (Active) Region
JFET becomes a good conductor and is controlled by the Gate-Source voltage while the Drain-Source voltage has little or no effect.
Breakdown Region
Voltage between the Drain and the Source is high enough to cause the resistive channel to break down and pass uncontrolled max current