## Slide 1: Robot Imaging
CAC 240
Anthony Winchester

## Slide 2: How Does A Robot “See”?
Machine Vision
The science of how a robot sees the environment around it
Visual Sensors
Infrared (IR) LED Transmitters
Infrared (IR) detector modules
Ultrasonic Sensors
Also known as sonar
Based on time taken to measure sound travel

## Slide 3: More about Visual Sensors
Most useful is the Infrared (IR) Sensor
One of the common Active Sensors used for robots
  Emitter that produces signal
  Detector that perceives the signal
Variety of types of IR sensors
  IR range sensors: Measure distances to objects
  IR proximity sensors: Replace physical contact sensors
  Passive Infrared (PIR) sensors: Detect motion based on detecting heat radiated by a body
  Data Transmission IR sensors: Transmit signals either between robots or with a stationary beacon or base
We will discuss IR Range Sensors, which can detect and avoid items from a certain distance

## Slide 4: Infrared (IR) Transmitters and Receivers

## Slide 5: Infrared (IR) LED Transmitter
Device that emits a beam of light in the infrared range
Designed for short-distance detection
Usually sold in pairs
  Transmitter: transparent
  Receiver: dark blue

## Slide 6: How IR Transmitters Work
IR LEDs in transmitter flash using a 555 timer at high frequency
Avoids interference with other sources of infrared light
Matches up with the infrared sensor
IR photons rebound off objects in the path of the robot and reflect to the IR receiver (detector)
Receiver will detect the signal (if something in path) and turn LED on

## Slide 7: Obstacle Avoiding Robot with IR LED and Sensor

## Slide 8: Infrared (IR) Receiver
IR receiver captures reflected light sent out by transmitter
Voltage measured based on the amount of light received
Advantage:
  Prices of these sensors are very reasonable
Disadvantages:
  IR sensors perform poorly in strong sunlight
  Many applications where this type of sensor is used are only for indoor use

## Slide 9: Components and Connections
Layout of the components behind the Infrared (IR) LEDs

## Slide 10: PIN Layout

## Slide 11: It is now time to build a schematic together
Let us Go to TinkerCad