## Slide 1: Photoresistors
CAC 240
Anthony Winchester

## Slide 2: Before we test the photoresistors…
…we need to know what they are and how they operate

## Slide 3: What is a Photoresistor?
Passive component that detects light and changes circuit operation depending on the level of light on its sensitive surface
When light intensity increases, then the photoresistor decreases its resistance
Also known as:
Light dependent resistor
LDR
Photocell
Photoconductor

## Slide 4: Sample Photoresistor
This is a photo of a sample light dependent resistor
Most photoresistors have metal contacts up top with a pattern across to take in the light

## Slide 5: Where are Photoresistors Found?
Found in a wide variety of items:
  Camera light meters
  Fire / smoke alarms
  Clock radios
  Alarm devices (as the detector for a light beam)
  Nightlights
  Outdoor clocks
  Solar street lamps
  Solar road studs
  Laser-based security systems
    Detects changes in light intensity when a person/object passes through the laser beam

## Slide 6: How does a Photoresistor Operate?
Electrical current consists of the movement of electrons within a material
  Conductors have a large number of free electrons
  Insulators with a high resistance have very few free electrons
Photoresistors have high resistance because there are very few electrons free and able to move
  Most electrons are locked into the photoresistor’s crystal lattice and unable to move

## Slide 7: How does a Photoresistor Operate? (continued)
Light falls on the semiconductor of the photoresistor
Light photons are absorbed by the semiconductor lattice and energy is transferred to the electrons
This new energy from the light breaks the electrons free from the crystal lattice – making them available to conduct electricity

## Slide 8: Now we are ready to run a photoresistor test
Take note:
ADC = analog-to-digital conversion
Analog light hitting photoresistor and sending digital output to screen

## Slide 9: Photoresistor Test
Enter the following commands in the Raspberry Pi terminal to test ADC module for light tracking:
  cd ~/Freenove_4WD_Smart_Car_Kit_for_Raspberry_Pi/Code/Server <press enter>
  sudo python test.py ADC <press enter>
Result:
  Every second, the voltage values of the two photoresistors and the battery are output
  When you shine a cell phone light on the photoresistors, take note of what happens with the voltage values on the screen
  NOTE: When you are just starting up the Raspberry Pi, these values may be inaccurate at first. The values will become stable later. Press "Ctrl + C" to end execution