## Slide 1: Final Project Discussion
CAC 240
Anthony Winchester

## Slide 2: Reducing Voltages for Measurement
One of the most fundamental circuits in electronics
Simple circuit which turns a large voltage into a smaller one
Using just two series resistors and an input voltage, we can create an output voltage that is a fraction of the input voltage
Never to be used to supply power to a load
  Current for load must run through resistor, and power produced dissipated in the form of heat – can melt resistor if power exceeds the rating of the resistor
  Voltage-divider-power-supply is very inefficient

## Slide 3: Formula for Voltage Divider
Output voltage is directly proportional to the input voltage and the ratio of R1 and R2
R1 is the resistor closest to the input voltage
R2 is the resistor closest to Ground

## Slide 4: Items needed for building voltage divider
These are listed in assignment specifications:
  Raspberry Pi
  Breadboard
  Jumper wires
  MCP3008 eight-channel Analog-to-Digital Converter (ADC) Integrated Circuit (IC)
  10kΩ resistor
  3.3kΩ resistor
  9V battery and clip lead

## Slide 5: MCP3008 Analog to Digital Converter Integrated Chip
Chip we will be using for our voltage divider

## Slide 6: MCP3008 Pin Configuration
Pin Number | Pin Name | Description
1,2,3,4,5,6,7,8 | Analog Input Channels | These are the 8 input pins, to which the analog voltage which has to be measured is provided
9 | Digital Ground | Connected to the Ground of the circuit
10 | Chip Select / Shutdown(CS`/SHDN) | This pin is connected to GPIO pin or MCU for turning on or off the IC
11 | Serial Data In (DIN) | Used for SPI communication
12 | Serial Data Out (DOUT) | Used for SPI communication
13 | Serial Clock (CLK) | Used to provide clock signal for SPI communication
14 | Analog Ground | Connected to Ground of the reference voltage
15 | Reference Voltage (VREF) | Connected to reference voltage for ADC Conversion
16 | Digital Voltage (Vdd) | Connection to apply positive voltage to the circuit

## Slide 7: Something to Note
Measure the battery before running your code
Run the code
Wait 5 minutes
Measure the battery again to see the potential difference
This is a display of the potential energy drain of a robot

## Slide 8: Code You will need
from gpizero import MCP3008
import time
R1 = 10000.0
R2 = 3300.0
analog_input = MCP3008(channel=0)
while True:
<your code goes here>

## Slide 9: What to submit in Moodle for grade
Copy of your code (in .py format)
Video of code execution results
Photo of voltage divider