## Slide 1: Optimizing Flight
By: Ty Armstrong

## Slide 2: Gliders Origin
Sir George Cayley (1773-1857)
First glider in 1804
Separate systems for lift and control which is similar to modern planes.

## Slide 3: Glide Planes
No engine with a small body and large wings.
Wings are slightly tilted to create lift for the plane.
Wings and body also create drag.
Pilots use updrafts to gain distance of flight.
Notes: This process is called pirouetting.

## Slide 4: Presented Question
What is the best speed to travel at to maximize the distance flown?

## Slide 5: Quantities of Importance
(Horizontal Airspeed)
(Vertical Airspeed)
(Ground Speed)
(Glide Ratio)
Notes: Represented by the vectors horizontal speed and ground speed are essentially the same. Ground speed is calculated by the speed of the planes shadow on the ground. The magnitude or the vertical airspeed is not as sharp because the plane is gliding in a horizontal fashion to maximize the height of the plane. Larger glide ratio indicates a better plane

## Slide 6: Polar Curve Graph
Stalls occur on the graph when a tangent line of slope zero is drawn on one of the curves. As seen when the planes airspeed approaches 0.
As the plane approaches a speed of zero the planes sink rate increases dramatically.
Optimal flight is flying slower in lift and speeding up through sink to maximize lift on the plane. This will maximize the distance at which the plane travels.
Notes: Pilots can determine their glider’s best glide airspeeds by drawing a tangent line to the gliders polar curve. When S (Downward air speed) is less than 0 the pilot will simply move the graph up by that S amount. Moving the origin up is the same as translating the polar curve down. Thus, when flying in a sink the best glider airspeed can be determined by taking the tangent line of the polar curve after moving the origin. Read from right to left.

## Slide 7: Minimizing Sink Rate
The author is trying to solve .
Using a quadratic model to determine the change in the change of the authors determine a formula.
This formula is used to determine the speed at which to travel to minimize the sink rate of the plane.
Notes: f(v_a) represents the speed to minimize the sink rate of the plane. Using a method of linear regression the authors use a graphing calculator to determine a best fit quadratic for the L-13 polar curve data as seen previously. Then using calculus they solve for the equation as the V_y function. This equation is used to determine the optimal speed to fly at while in sink as the glider. The sink rate of the glide plane is being minimized because the more efficient sink rate will yield a farther distance traveled.

## Slide 8: Determining an Optimal Speed for Gliding
Authors use the maximum glide ratios which is determined by calculus. This ratio is plotted as the green line.
Graphing the gliders flight over time as the black line the point of intersection (critical point) indicates the optimal flying speed to maximize the distance the plane travels.
These speeds are then applied to the glide ratios to determine the best plane to buy which is indicated by the largest glide ratio.
Notes: This is just putting the previous slide in graphical terms where the best fit curve is displayed as the black line and the green line represents the maximum glide ratio which is derived from calculus using the values seen in the table previously. Critical point is th point that lies tangent to the best fit curve. This point tells the horizontal airspeed and vertical airspeed at which the glider should be traveling at normally to maximize distance flown.

## Slide 9: In Numerical Terms
S (Sink Rate)
H (Tail winds )
Applying the knowns to the equations and solving for we see X , speed to fly through sink is greater than while slower with tailwind.
These values are determined by the vertical and horizontal tangent lines seen on the graph
Notes: S shifts the critical point of the graph seen previously up by S since S is the sink rate. In summary the pilots simply determine the critical point of the polar curve and glide ratio. Then making a line horizontal and vertical they can determine the optimal speeds at which they should fly horizontally and vertically. Optimizing these speeds with the equations when variables such as S (vertical shift) and H( horizontal shift) above we can determine the best speed to fly during sink and with tailwinds. The equations are oriented to maximize the distance a plane will fly by determining the best flight speeds through different intervals. Using the critical point from the graph the third equation can be solved for X. We can then plug in this X to the rest of the equations to determine the best horizontal and vertical airspeed to glide at when experiencing tail winds and and sink rate. Now the airspeed to travel has been solved for involving every variable the glider may experience so in taking the date the best plane can be determined.

## Slide 10: Results
The results show the optimal flying speeds of the planes in consideration and display the best plane to use based on the methods presented.
They determined that the LS 13 was the best plane to buy due to its high airspeed and lack of stall points while being in the middle of the pack in terms of price.
The LS 13 also had the maximum distance able to travel not taking into account the skills of the pilot.
The authors concluded that when buying a glider plane the more expensive option is often not the better choice.

## Slide 11: Comments/Future Research
The authors fail to consider the addition or subtraction of weight.
Seen mostly in racing glider planes, water is often stored in capsules on the plane to increase the plane’s horizontal airspeed when descending. This in turn creates a farther distance traveled.
This is not considered in determining an optimal glider that maximizes the distance it can travel.

## Slide 12: References
Lundin, Michael A. “Optimal Soaring: What Is the Best Speed to Fly?” Math Horizons, vol. 15, no. 4, 2008, pp. 12–15. JSTOR, http://www.jstor.org/stable/25678750. Accessed 11 Oct. 2023.